## Slide 1
Water Quality Monitoring & Eutrophication Risk Tool
A physicochemical scoring model for freshwater pond assessment
MSc Environmental Monitoring Project | 2025

## Slide 2
Why Does Eutrophication Matter?
Excess nutrients (phosphorus & nitrogen) from agricultural runoff cause rapid algal blooms
Algal decomposition consumes dissolved oxygen, triggering hypoxia and fish kills
Harmful cyanobacteria toxins contaminate water and restrict recreational use
Internal phosphorus release from sediments can keep ponds locked in a polluted state
Nutrient-rich outflows spread eutrophication to connected streams and lakes downstream
Source: Environmental monitoring literature and MSc experimental data

## Slide 3
13 Physicochemical Parameters Monitored
Each parameter reflects a different dimension of pond health
NUTRIENTS
Phosphate (PO₄³⁻)
Nitrate (NO₃⁻)
Total Nitrogen
Ammonia (NH₃)
OXYGEN & REDOX
Dissolved Oxygen (mg/L)
Dissolved Oxygen (%DO)
ORP (mV)
WATER PROPERTIES
pH
Temperature (°C)
Conductivity (EC)
TDS
Salinity (PSU)
Chlorophyll A

## Slide 4
Weighted Water Quality Score (WQS)
WQS = Σ (Parameter Score × Weight) — normalised to 0–100
Dissolved Oxygen
20%
Phosphate
20%
Nitrate
15%
Chlorophyll A
15%
Ammonia
10%
Total Nitrogen
10%
Others combined
10%
Classification bands
80–100 Excellent
60–80 Good
40–60 Moderate
<40 Poor

## Slide 5
Interactive Assessment Tool
A browser-based tool — no installation required | Try it: [YOUR_URL_HERE]
Input
13 parameter input fields
Threshold hints per parameter
Preset scenarios: Healthy / Moderate / Eutrophic
Analysis
Real-time WQS calculation
Eutrophication risk engine (High / Moderate / Low)
Parameter-by-parameter classification
Visualisation
Animated arc gauge (0–100)
Colour-coded parameter bars
Plain-English risk explanation
Built with HTML, CSS & JavaScript — accessible to all audiences

## Slide 6
What This Project Demonstrates
Technical Skills
Python data analysis & scoring model design
Excel workbook with live WQS formulas & scenarios
Interactive web tool development (HTML/CSS/JS)
Parameter threshold research & classification
Domain Knowledge
Freshwater eutrophication mechanisms
Physicochemical water quality assessment
Application of peer-reviewed parameter thresholds
Environmental monitoring & risk communication
All thresholds grounded in peer-reviewed literature: Boyd (2019), Carlson TSI (1977), Elser et al. (2022), US EPA, WHO, and MSc experimental data.